Chapter 29

On Deep Electroconductivity of Tobol-Ishim Interfluve

V. P. Borisova, T. A. Vasilieva, S. L. Kostuchenko and E. B. Fainberg

Abstract The results of ID and 2.5D modeling and inversion of amplitude and phase curves of magnetotelluric sounding in the Tobol-Ishim interfluve of Western Siberia are presented. Cross sections of the electrical conductivity of the crust and asthenosphere arc constructed as well. It is suggested that there is a conductive layer lying at a depth of ~ 60-70 km. A decrease in the electrical resistivity of the overlying crustal layer from 1000-3000 to — 300 Q-m which may be a sign of an increase in the conductivity of the earth's crust is noted.

J

Keywords Magnetotellurics • Western Siberia * Conductive layer

Prospecting magnetotelluric soundings in the southwest of the West Siberian Plate (WSP) have been carried out by the explorers of the Tyumen Geological Administration in 1980-1981 on one of the oil and gas promising areas of the Tobol-Ishim interfluve (Fig. 29.1).

The area of the MT survey is confined to the joint of the Caledonian folded Kazakhstan system (the western side of the Vagay-Ishim depression) and the Hercynian folded Ural system (the eastern side of the Tobolsk anticlinorium) and is located in the inter-rift area between the Nizhnetavdinsk and Ishim branches of the Triassic rift system (Fig. 29.2). MT profiles arc located mainly in the zone between two wedge-jointing deep faults (marginal seams) of the northeast strike—the Middle Paleozoic East Urals and Early Paleozoic Central Turgay—and cross a scries of Middle-Upper Paleozoic intra-structural faults also in the northeast direction. These include the well-pronounced Kiselevsky fault and the less extended Dronovsky fault. The faults are traced by features in the behavior of geophysical fields, crushing zones, chains of intrusions of the main and ultrabasic compositions.

V. P. Borisova • T. A. Vasilieva E. B. Fainberg (El)

GeoelectTo magnetic Research Centre—Schmidt Institute of Physics of the Earth.

Moscow. Russia e-mail: edfain@yandcx.ru

S. L. Kostuchenko

Limited Liability Company “Rosgeology", Moscow. Russia

© Springer Nature Switzerland AG 2019	249

D. Nurgaliev and N. Khairullina (eds.). Practical and Theoretical Aspects of Geological Interpretation of Gravitational, Magnetic and Electric Fields, Springer Proceedings in Earth and Environmental Sciences, https://doi.org/10.1007/978-3-319-97670-9_29